## Slide 1: ECHOP v1 Efficient Compact Header Optimization Protocol
Lightweight UDP-Based IoT Telemetry Protocol
CSE361 – Computer Networks Course Project
Abdelrahman Mostafa – Habiba Sherif – Mohamed Ashraf
Roger Sherif – Rowaida Emad – Somaya Ahmad
Supervised by: Dr. Ayman Bahaa Eldin | Eng. Noha Wahdan

## Slide 2: ECHOP v1 – Protocol Overview
Sessionless application-layer protocol built on UDP
10-byte fixed-size header for minimal overhead
Batching support for multiple sensor readings per packet
Smart payload compression (int32 vs float64)
Receiver-driven reliability using NACKs (no ACK flooding)

## Slide 3: System Architecture
Client (Sensor Node):
- Reads sensor data periodically
- Applies smart compression and encryption
- Sends DATA, INIT, and HEARTBEAT messages
Server (Collector):
- Tracks per-device sequence numbers
- Detects gaps and schedules NACKs
- Reorders packets using jitter buffer
- Logs results to CSV for analysis

## Slide 4: ECHOP v1 Header Format (10 Bytes)
DeviceID (4 bits) + BatchCount (4 bits)
Sequence Number (16 bits)
Timestamp (32 bits, UNIX epoch)
Protocol Version (2 bits)
Message Type (2 bits)
Millisecond sub-field (10 bits total)
Checksum (8 bits)

## Slide 5: Message Types
MSG_INIT: Session start and device registration
MSG_DATA: Carries compressed and encrypted sensor data
HEARTBEAT: Sent during idle periods to indicate liveness
NACK_MSG: Sent by server to request retransmission of missing packets

## Slide 6: Smart Payload Compression
Sensor values are scaled by 10⁶ to preserve precision
If scaled value fits in 32-bit signed integer → send int32
Otherwise → fallback to float64 (8 bytes)
Hybrid payload format with flags indicating float indices
Achieves 30–50% payload size reduction in typical scenarios

## Slide 7: Reliability Mechanism (NACK-Based)
Server tracks expected sequence number per device
If received Seq > expected → gap detected
NACK is delayed (350 ms) to tolerate packet reordering
Client retransmits exact packet from history buffer
Avoids per-packet ACK overhead and reduces congestion

## Slide 8: Packet Reordering & Jitter Handling
UDP packets may arrive out of order under network jitter
Server inserts packets into a min-heap keyed by timestamp
Packets held for a guard time (≈150 ms)
Ensures correct temporal ordering before analysis and logging